## Slide 1
BACKGROUND
CONCLUSIONS
INTRODUCTION
FUTURE RESEARCH
RESULTS
ACKNOWLEDGEMENTS
REFERENCES
We are especially thankful for the support and assistance of the Augusta University Team, especially:
Dr. T. DeSilva for mentorship in theoretical quantum physics,
Dr. T. Colbert for mentorship in experimental methods,
Dr. J.A. Hauger for electronics and micro-computing assistance,
Dr. J. Newton for assistance and mentorship with nuclear theory,
Dr. N. Yanasak for assistance with programming image processing,
Mr. O. Angelton for assistance with laboratory materials, and
Mr. W. Cooke for assistance with system integration.
Video Media and
Complete Experiment Notes
Khang Kieu and Andrew Liebig, Department of Chemistry and Physics, College of Science and Mathematics
Cloud Chamber Optical Measurement of Nuclear Decay
In future research, we plan to:
Construct acrylic or engineered glass chamber enclosure
Integrate and program thermocouple and heating elements
Improve video capture methods to pursue optical counting
Study alternate radioisotope sample sources
Fig 7: Possible future projects would study needle sources as calibration to measure activity in natural uranium sources
We identify characteristic Am-241 and Th-232 alpha decay phenomena that manifest as condensation trails in the vapor
Improved conditions are needed to produce favorable imaging conditions or identify a proportional count rate
We construct a cloud chamber and perform video analysis to identify and characterize decay phenomena
We optimize conditions to identify ideal system arrangement for imaging decay and measure source disintegrations in the cloud chamber
Cloud Chambers were first developed by Charles Thomson Rees Wilson and applied in experimental analysis in 19121
A Cloud Chamber uses temperature gradient in a sealed chamber. The gradient helps create a region of air supersaturated with isopropyl vapor
Radioisotope source disintegrations emit charged particles which transfer energy to the supersaturated vapor2
Decay energy and particle mass produce phase transitions with characteristic condensation vapor trails3
Laterally angled illumination increases visible contrast in decay trails for video analysis3
Particles from atomic disintegrations become visible by unassisted eye
EXPERIMENTAL PROCEDURE
1 Britannica, T. Editors of Encyclopaedia (2023, February 10). C.T.R. Wilson. Encyclopedia Britannica. https://www.britannica.com/biography/C-T-R-Wilson
2 Interview of Luis Alvarez by Charles Weiner and Barry Richman on 1967 February 14, Niels Bohr Library & Archives, American Institute of Physics, College Park, MD USA, www.aip.org/history-programs/niels-bohr-library/oral-histories/4483-1
3 B. Allison, Particle physics -cloud chambers activities for
schools (2012), https://www.birmingham.ac.uk.
4 National Nuclear Data Center. "NuDat 3.0 database". Brookhaven National Laboratory. https://www.nndc.bnl.gov/nudat3/
We observe Alpha Decay phenomenon in Tungsten Thoriated Rods and Americium.
FIG 2: Th-232 Source
Fig 1: Am-241 Source
Raspberry Pi 4 controls electronic components
Illumination with programmable LEDs
Power management with programmable relays
High Voltage Generator creates an electric field, increases ionizations and contrast
Imaging with Pi Controlled Camera
Image Processing with MATLAB
FIG 4: Camera and Single board computer
Creating the Temperature Gradient
  Internal electrical heaters increase the temp of an isopropyl alcohol reservoir to 100°C and external ceramic heaters increase surface temp to 85°C
Dry ice cools the steel base plate down to -60°C and condenses alcohol vapor to form droplets
FIG 3: Voltage Source Screen, Alcohol heater and Lighting assembly
1
5
2
3
4
6
7
9
10
13
11
12
FIG 5: Image series of Th-232 characteristic 4.08 MeV alpha decay shows two charged energetic particles causing ionization and disrupting transport4
FIG 6: Image series of Am-241 characteristic 5.64 MeV alpha decay shows several simultaneous decay tracks
Am-241 shows a higher rate of ionization, which agrees with the higher isotopic activity as compared to Th-232 (432.6 y for Am-241 and 14x109 y for Th-232) 4
8